## Slide 1
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
Chapter 4 Network Layer:
The Data Plane
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020

## Slide 2: Chapter 4: network layer
chapter goals:
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  how a router works
  addressing
  generalized forwarding
instantiation, implementation in the Internet
  IP protocol
  NAT
Generalized Forwarding and SDN

## Slide 3
Provides various forms of process-to-process communication by relying on the network layer’s host-to-host communication service.
The Network Layer
Overview
Transport layer
Can provide its host-to-host communication service.
the most complex layer in the protocol stack.
Network layer
Decomposed the network layer into TWO parts: Data Plane (Chapter 4) & Control Plane (Chapter 5)
4-3

## Slide 4
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
input ports, switching, output ports, buffer management, scheduling
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation (NAT)
  IPv6
4.4 Generalized Forwarding and SDN
  Match+action
  OpenFlow: match+action in action
Chapter 4: data plane

## Slide 5: Network layer services and protocols
transport segment from sending to receiving host
  sender: encapsulates segments into datagrams, passes to link layer
  receiver: delivers segments to transport layer protocol
network layer protocols in every Internet devices: hosts, routers
routers
  router examines header fields in all IP datagrams passing through it
  moves datagrams from input ports to output ports to transfer datagrams along end-end path
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 6: Two key network-layer functions
Determine route taken by packets from source to destination.
* routing algorithms
Move packets from router’s input to appropriate router output.
Analogy:
Routing: Process of planning trip from source to destination.
Two Functions
1st: Forwarding
2nd: Routing
Analogy:
Forwarding: process of getting through single interchange.
forwarding
routing

## Slide 7: Two key network-layer functions
Interplay between forwarding and routing
Figure: Routing algorithm determine values in forwarding tables
Forwarding:
Determines local forwarding for this router.
Routing:
Determines end-to-end path through network

## Slide 8: Network layer: data plane, control plane
Data plane
Forwarding function: Determines how datagram arriving on router input port is forwarded to router output port.
Local, per-router function.
Control plane
Routing function: Determines how datagram is routed among routers along end-end path from source host to destination host.
Network-wide logic.
(Software-Defined Networking SDN)
Implemented in server (remote)
Implemented in routers.
Two Control-Plane Approaches
Traditional Routing Algorithms
SDN
Network Layer: 4-8
1
2
3
0111
values in arriving
packet header

## Slide 9: Datagram forwarding table
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
4 billion IP addresses, so rather than list individual destination address,
list range of addresses
(aggregate table entries)
2 = 4,294,967,296
32
IPv4:

## Slide 10
Forwarding and Routing
Kurose, J.F. and Ross, K.W. (2021). Computer Networking: A Top-Down Approach (8th Edition). Pearson Education Limited, England. (pp. 307)
Figure: Routing algorithm determine values in forwarding tables
Per-router control plane
The Traditional Approach
Forwarding:
Determines local forwarding of this router.
Routing:
Determines end-to-end path through network.
Individual routing algorithm components in each and every router interact in the control plane

## Slide 11
Forwarding and Routing
(b) The SDN Approach
Forwarding:
Determines local forwarding of this router.
Routing:
Determines end-to-end path through network.
Figure: A remote controller determines and distributes values in forwarding tables
Software-Defined Networking (SDN)
Remote controller computes, installs forwarding tables in routers

## Slide 12: Network service model
Q: What service model for “channel” transporting datagrams from sender to receiver?
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing

## Slide 13: Network-layer service model
Network
Architecture
Internet
ATM
ATM
Internet
Internet
Service
Model
best effort
Constant Bit Rate
Available Bit Rate
Intserv Guaranteed
(RFC 1633)
Diffserv (RFC 2475)
Bandwidth
none
Constant rate
Guaranteed min
yes
possible
Loss
no
yes
no
yes
possibly
Order
no
yes
yes
yes
possibly
Timing
no
yes
no
yes
no
No guarantees on:
  successful datagram delivery to destination
  timing or order of delivery
  bandwidth available to end-end flow
Internet “best effort” service model
Quality of Service (QoS) Guarantees ?

## Slide 14: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Quality of Service
(QoS) Guarantees ?
Asynchronous Transfer Mode (ATM) - Network Architecture
CBR: Constant Bit Rate, VBR=Variable Bit Rate, ABR=Available Bit Rate, UBR= Unspecified Bit Rate

## Slide 15: Reflections on best-effort service:
simplicity of mechanism has allowed Internet to be widely deployed adopted
sufficient provisioning of bandwidth allows performance of real-time applications (e.g., interactive voice, video) to be “good enough” for “most of the time”
replicated, application-layer distributed services (datacenters, content distribution networks) connecting close to clients’ networks, allow services to be provided from multiple locations
congestion control of “elastic” services helps
It’s hard to argue with success of best-effort service model

## Slide 16
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
input ports, switching, output ports
buffer management, scheduling
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation (NAT)
  IPv6
4.4 Generalized Forwarding and SDN
  Match+action
  OpenFlow: match+action in action
Chapter 4: data plane

## Slide 17: Router architecture overview
TWO key router functions:
run routing algorithms / protocol (RIP, OSPF, BGP)
forwarding datagrams from a router’s incoming links to the appropriate outgoing links at a router
Figure: Four router components
Router
Input Ports
Output Ports
Switching Fabric
Routing Processor
RIP (Routing Information Protocol)
OSPF (Open-Shortest Path First)
BGP (Border Gateway Protocol)
Four router components can be identified:

## Slide 18: Router architecture overview
high-speed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operates in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
high-level view of generic router architecture:

## Slide 19
The forwarding table (FT) is computed and updated by the routing processor
Lookup performed
in the input port
forwarded via the
switching fabric
Packet arrives
36
Why shadow copy?
forwarding decisions done locally (at input port)
avoiding bottleneck at central processor
a shadow copy of
FT is stored at each
input port
Router architecture overview

## Slide 20: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 6
switch
fabric

## Slide 21: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding (SDN): forward based on any set of header field values
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 6
switch
fabric

## Slide 22: Destination-based forwarding
Q: but what happens if ranges don’t divide up so nicely?
3
Network Layer: 4-22
Notes: Text for this animation:
This all works out pretty nice and looks pretty simple!
But of course the devil is in the details, as the saying goes.
What happens, for example, when a subset of addresses say in this first range should go to say interface 3, rather than interface 0. Well, of course we could split the first address range into multiple pieces, and add in this new subrange with its new destination output port. But it turns out there’s a much simpler and elegant way to do this. Known as longest prefix matching.

## Slide 23: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
11001000 00010111 00010110 10100001

## Slide 24: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 25: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 26: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 27: Longest prefix matching
we’ll see why longest prefix matching is used shortly, when we study addressing
longest prefix matching: often performed using ternary content addressable memories (TCAMs)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: can up ~1M routing table entries in TCAM

## Slide 28
Transfer packet from input link to appropriate output link
Switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate.
  N inputs: switching rate = N times line rate desirable.
Switching Fabrics
high-speed
switching
fabric
N input ports
N output ports
. . .
. . .
R
R
R
R
(rate: NR, ideally)

## Slide 29: Switching fabrics
transfer packet from input link to appropriate output link
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 30: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 31: Switching via memory
Switching Fabrics
Datagram
arrives
Processor copy
datagram into Memory
Check Dest
Lookup FT
Copy datagram
to output port

## Slide 32: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 33: Switching via a bus
Datagram arrives
Datagram gets switch label
Datagram gets
on bus
The correct output port get it  strip label  send on its ways

## Slide 34: Switching via interconnection network (crossbar)
overcome bus bandwidth limitations
Crossbar, Clos networks, other interconnection nets initially developed to connect processors in multiprocessor
8x8 multistage switch
built from smaller-sized switches
3x3 crossbar
multistage switch: nxn switch from multiple stages of smaller switches
exploiting parallelism:
  fragment datagram into fixed length cells on entry
  switch cells through the fabric, reassemble datagram at exit
3x3 crossbar

## Slide 35: Switching via interconnection network (crossbar)
scaling, using multiple switching “planes” in parallel:
  speedup, scaleup via parallelism
fabric plane 0
. . .
. . .
fabric plane 1
. . .
. . .
fabric plane 2
. . .
. . .
fabric plane 3
. . .
. . .
fabric plane 4
. . .
. . .
fabric plane 5
. . .
. . .
fabric plane 6
. . .
. . .
fabric plane 7
. . .
. . .
Cisco CRS router:
  basic unit: 8 switching planes
  each plane: 3-stage interconnection network
  up to 100’s Tbps switching capacity

## Slide 36: Switching via interconnection network (crossbar)
45
Datagram arrives
Check dest. (Y)
Close A-Y  put datagram on bus
Y picks up
datagram

## Slide 37: Input port queuing
If fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 38: Output port queuing
Buffering required when datagrams arrive from fabric faster than link transmission rate. Drop policy: which datagrams to drop if no free buffers?
Scheduling discipline chooses among queued datagrams for transmission
Datagrams can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality
line
termination
link
layer
protocol
(send)
switch
fabric
(rate: NR)
datagram
buffer
queueing
R

## Slide 39: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 40: How much buffering?
RFC 3439 rule of thumb:
  average buffering size = RTT * link capacity C
  e.g., RTT=250 msec (“typical”), C = 10 Gpbs link
    average buffering size =250 msec * 10 Gpbs
              = 2.5 Gbit buffer
More recent recommendation: with N flows, buffering equal to
RTT C
.
N
but too much buffering can increase delays (particularly in home routers)
  long RTTs: poor performance for realtime apps, sluggish TCP response
  recall delay-based congestion control: “keep bottleneck link just full enough
  (busy) but no fuller”

## Slide 41
Supposed the link capacity for a router is 20Mbps and RTT for a packet is 400msec.
If the TCP flow of packets is 16, calculate the buffering needed for the router.
Exercise
Solution:
Link capacity, C = 20Mbps
RTT = 400msec
TCP flows, N = 16
Buffer size,

## Slide 42: Buffer Management
buffer management:
drop: which packet to add, drop when buffers are full
  tail drop: drop arriving packet
  priority: drop/remove on priority basis
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
scheduling
marking: which packets to mark to signal congestion (ECN, RED)
R
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)
Abstraction: queue
R

## Slide 43
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
input ports, switching, output ports
buffer management, scheduling
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation (NAT)
  IPv6
4.4 Generalized Forwarding and SDN
  Match+action
  OpenFlow: match+action in action
Chapter 4: data plane

## Slide 44: Network Layer: Internet
host, router network layer functions:
IP protocol
datagram format
addressing
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer
forwarding
table
Path-selection algorithms: implemented in
routing protocols (RIP, OSPF, BGP)
SDN controller
RIP (Routing Information Protocol)
OSPF (Open Shortest path First)
BGP (Border Gateway Protocol)

## Slide 45: IP Datagram format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
diffserv (0:5)
ECN (6:7)
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
e.g., timestamp, record route taken
32-bit source IP address
32-bit destination IP address
header checksum
Maximum length: 64K bytes
Typically: 1500 bytes or less

## Slide 46: IP datagram format
Understanding datagram format is important
A datagram has its own header (overhead)  20 bytes
A datagram holds TCP/UDP segment within it  TCP/UDP has own overhead
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead for TCP+IP
overhead
Notes: Recall that a network-layer packet is referred to as a datagram

## Slide 47: IP datagram format
IPv4 Datagram Format
20 bytes

## Slide 48: IP fragmentation, reassembly
network links have MTU (max.transfer unit) - largest possible link-level frame
  different link types, different MTUs
  Ethernet MTU 1500 bytes
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 49: IP fragmentation, reassembly
Fragmentation:
Reassembly:
= 4000 / 1500 bytes
= 3 datagrams
Original datagram :
4000 bytes
= 20 bytes of IP header
+ 3,980 bytes of IP payload
IP fragmentation, reassembly

## Slide 50: IP fragmentation, reassembly
IP fragmentation, reassembly
length=1500 ID=777 flag=1 offset=0
Fragment #1
length=1500 ID=777 flag=1 offset=185
Fragment #2
length=1040 ID=777 flag=0 offset=370
Fragment #3

## Slide 51: IP fragmentation, reassembly
Offset value specified in units of 8-byte chunks
Fragment 1
Fragment 2
Fragment 3
0
8
...
1472
1480
...
2952
2960
...
3980
0
185
370
offset:
Why 1480 not 1500?
Data (1480) + Header (20) = 1500 bytes
Fragments of same datagram
IP fragmentation, reassembly

## Slide 52
A datagram of 5000 bytes arrived at a router and must be forwarded to a link with an MTU of 1500 bytes. Suppose that the original datagram is stamped with an identification number of 333. Draw all IP fragments generated after fragmentation that reflect the requirement of original payload data in the datagram.
Exercise
length=5000 ID=333 flag=0 offset=0
Datagram

## Slide 53
Solution:
20 header + 4980 data
Solution
length=1500 ID=333 flag=1 offset=0
Fragment#1
length=5000 ID=333 flag=0 offset=0
Datagram
Total fragments = 5000 / 1500 = 4
4980 = 1480 + 1480 + 1480 + 540
length=1500 ID=333 flag=1 offset=185
Fragment#2
length=1500 ID=333 flag=1 offset=370
Fragment#3
length= 560 ID=333 flag=0 offset=555
Fragment#4

## Slide 54
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
input ports, switching, output ports
buffer management, scheduling
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation (NAT)
  IPv6
4.4 Generalized Forwarding and SDN
  Match+action
  OpenFlow: match+action in action
Chapter 4: data plane

## Slide 55
IPv4 Addressing
What is an IP Address?
IP address is used to identify a host within a network.
  are written in a so-called dotted decimal notation
  Each byte is identified by a decimal number in the range [0…255]:
Example:

## Slide 56
Interface: connection between host/router and physical link.
IPv4 Addressing
Addresses
IP address: 32-bit identifier for each host or router interface
  router's typically have multiple interfaces.
  host typically has one or two interfaces. (e.g., wired Ethernet, wireless 802.11)
One IP address associated with each interface !

## Slide 57
IPv4 Addressing
Q: How are interfaces
actually connected?
A: wired Ethernet interfaces connected by Ethernet switches (Link Layer)
A: wireless WiFi interfaces connected by WiFi base station (AP – access point)
Addresses

## Slide 58: IPv4 Addressing – Subnet/Subnetting
Notes: STOP HERE!!! Sec 01 – 17.04.17 ( Monday ) ; 4pm

## Slide 59
IPv4 Addressing
Subnets
  Interconnecting three host interfaces and one router interface forms a subnet.
device interfaces that can physically reach each other without passing through an intervening router
is a logical, visible subdivision of an IP network. The practice of dividing a network into two or more networks is called subnetting.
What’s a subnet ?

## Slide 60
A subnet is a group of host identified with having the same network portion of their IP address
Example:
  223.1.1.1, 223.1.1.2, 223.1.1.3, 223.1.1.4, …
223.1.1.1, 223.1.1.2, 223.1.1.3, 223.1.1.4, …
This network portion is indicated by the subnet mask with notation /24
Subnet mask defines the subnet address
  ➙ 223.1.1.0/24
IPv4 Addressing
Subnets
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
Network consisting of 3 subnets

## Slide 61
A computer OR a router must be able to identify whether a host with a given IP address is on its subnet or not.
The subnet mask is:
  used to separate the network portion of an IP address from the host portion.
  a set of 32 bits IP address which the bits in the network portion of the address are set to 1s and the host portion is set to 0s.
IPv4 Addressing
Subnet Mask

## Slide 62
Thus, subnet mask = 255.255.255.0
IPv4 Addressing
Subnet Mask
Network portion
Host portion
11111111
11111111
11111111
00000000
8 bits 8 bits 8 bits 8 bits
IP address with w.x.y.z /24 address.

## Slide 63
Each IP address can be divided into network portion and host portion
  Network portion (indicated by subnet mask)
    all host with same network portion are in the same subnet
    these host can physically reach each other without intervening router
  Host portion (the remaining bits  {32 bits – subnet mask })
    The individual (unique) address for a host
  Example: 192.64.22.31/24
11000000 . 01000000 . 00010110 . 00011111
192
64
22
31
Network portion
Host portion
IPv4 Addressing
Subnet Mask

## Slide 64
Convert these subnet mask into decimal values.
(a) /8
(b) /16
(c) /24
(d) /25
11111111.00000000.00000000.00000000
255.0.0.0
11111111.11111111.00000000.00000000
255.255.0.0
11111111.11111111.11111111.00000000
255.255.255.0
IPv4 Addressing
Subnet Mask
Example
11111111.11111111.11111111.10000000
255.255.255.128

## Slide 65
Given the information we find that:
  The host portion has 8 bits 
    this subnet can have up to 28 = 256 hosts
    With IP addresses ranging from 192.64.22.0 – 192.64.22.255
  But the first and last IP address cannot be assigned to host
    so only 254 hosts available (or usable)
    …thus useable IP addresses  192.64.22.1 – 192.64.22.254
  The first IP – becomes network address  to address the subnet
  The last IP – becomes broadcast address  used to broadcast info throughout the subnet
11000000 . 01000000 . 00010110 . 00011111
192
64
22
31
Network portion
Host portion
192.64.22.31/24
IPv4 Addressing

## Slide 66
Given an IP address and subnet mask, we can find the network address and broadcast address …
Example: IP address = 192.168.1.10/24
  Set the host portion as all zero(0) to get network address
  Set the host portion as all one(1) to get broadcast address
192.168.1.10
192.168.1.[00000000]
Network address: 192.168.1.0
192.168.1.[11111111]
Broadcast address: 192.168.1.255
IPv4 Addressing
Subnet Network Address (Binary Method) and Broadcast Address

## Slide 67
IPv4 Addressing
Subnet Network Address (AND Method)
To determine subnet address:
IP address AND subnet mask
(AND)
Example:
If the subnet mask is 255.255.255.0, define the subnet address.
223.1.1.0/24
223. 1 . 1 .4
AND 255.255.255.0
11011111.00000001.00000001.00000100
11111111.11111111.11111111.00000000
11011111.00000001.00000001.00000000
223.1.1.0/24

## Slide 68
182.126.103.215/30
Network portion of the address DOES NOT CHANGE.
IPv4 Addressing
Example

## Slide 69
178.120.188.96/16
16 bits for the network portion and 16 bits for host portion
IPv4 Addressing
Example
Network portion of the address DOES NOT CHANGE.

## Slide 70
Given these IP addresses, determine the network portion and the host portion
  192.168.12.0/24
  192.168.12.25/25
  172.16.32.0/16
  172.16.32.0/20
  10.10.10.0/8
Class Exercise
In-class try out ...

## Slide 71
Type of Addressing
Classful ( old one)
Classless (CIDR) ( current)
IPv4 Addressing – Type of Addressing

## Slide 72
In the beginning, addressing scheme known as classful addressing 
  where IP blocks were given according to size
  Class A – big size of organization
  Class B – medium size of organization
  Class C – small size of organization
Classful Addressing

## Slide 73
Classful addressing

## Slide 74
Classful addressing
/8 255.0.0.0
/16 255.255.0.0
/24 255.255.255.0

## Slide 75
Classful addressing
  Example:
  An organization needs 2000 hosts and apply class B
  Class B allocated 65000 addresses, and leaving more than 63000 not used.
  PROBLEMS: Wasted addresses and not optimized
  Large organizations do not fully utilize the IP address they have
  Had problem supporting the rapidly growing number of organizations with small and medium-sized subnets

## Slide 76
  more flexible than original system of internet address scheme (classful addressing), subnet portion of address of arbitrary length
  can avoid situations where large numbers of IP addresses are unused
  address format: a.b.c.d/x
200.23.16.0/23
11001000.00010111.00010000.00000000
Subnet part
host
part
Classless Inter Domain Routing (CIDR)
where x is no. of bits in subnet portion of address often referred to as prefix
Network part

## Slide 77
Example:
  An organization needs 2000 hosts and apply for IP address
  Host needed is 2000  211 = 2048 (i.e. only extra 48)
  Thus an IP address 163.44.224.0/21 is given
    How we get … /21 ?  32 – 11 = 21
Classless Inter Domain Routing (CIDR)
Network portion
Host portion
11111111
11111111
11111
00000000000
21 bits 11 bits

## Slide 78
Q: How does a network get subnets part of an IP address?
A: by subnetting the given IP address
Example: 200.23.16.0/20 to be divided into 8 subnets (23).
ISP’s block:
200.23.16.0/20 
11001000.00010111.00010000.00000000
Subnet 0:
200.23.16.0/23 
11001000.00010111.00010000.00000000
Subnet 1:
200.23.18.0/23 
11001000.00010111.00010010.00000000
…
Subnet 7:
200.23.30.0/23 
...
11001000.00010111.00011110.00000000
Subnetting: To subnet a small network
Host portion
Network portion
need to borrow 3 bits
from host portion
to define 8 subnets

## Slide 79
Say, Company A (CA) is given the IP address 192.168.1.0/24
CA has 4 departments under it:
  RND
  Sales
  Finance
  Human Resource (HR)
CA decided to divide the network according to purpose. So, the network needs to have 4 subnets.
Subnetting (Example): To subnet
a small network

## Slide 80
192.168.1.0/24 to be divided into 4 subnets
192.168.1.0/24 
11000000.10101000.00000001.00000000
Subnetting (Example): To subnet
a small network

## Slide 81
192.168.1.0/24 to be divided into 4 subnets
192.168.1.0/24 
11000000.10101000.00000001.00000000
need to borrow 2 bits
from host portion
to define 4 subnets
(i.e. 22)
Host portion
Network portion
11000000.10101000.00000001.00000000
Subnet address: 
Subnetting (Example): To subnet
a small network

## Slide 82
192.168.1.0/24 to be divided into 4 subnets
192.168.1.0/24 
11000000.10101000.00000001.00000000
11000000.10101000.00000001.00000000
Host portion
Network portion
Subnet address: 
11000000.10101000.00000001.00000000
Subnet 0: 
192.168.1.0/26
The subnet mask for each subnet
is /26 OR 255.255.255.192
6 bit left for host
Subnetting (Example): To subnet
a small network

## Slide 83
11000000.10101000.00000001.00000000
Subnet 0: 
192.168.1.0/26
192.168.1.[ 00 000000 ]
.[ 00 111111 ]
.[ 01 000000 ]
.[ 01 111111 ]
.[ 10 000000 ]
.[ 10 111111 ]
.[ 11 000000 ]
.[ 11 111111 ]
subnet 0
subnet 1
subnet 2
subnet 3
Subnetting (Example): To subnet
a small network

## Slide 84
Subnet 0: 
192.168.1.0/26
192.168.1.[ 00 000000 ]
.[ 00 111111 ]
.[ 01 000000 ]
.[ 01 111111 ]
.[ 10 000000 ]
.[ 10 111111 ]
.[ 11 000000 ]
.[ 11 111111 ]
subnet 0; network address = 192.168.1.0
subnet 1; network address = 192.168.1.64
subnet 2; network address = 192.168.1.128
subnet 3; network address = 192.168.1.192
11000000.10101000.00000001.00000000
Subnetting (Example): To subnet
a small network

## Slide 85
Subnet 0: 
192.168.1.0/26
192.168.1.[ 00 000000 ]
.[ 00 111111 ]
.[ 01 000000 ]
.[ 01 111111 ]
.[ 10 000000 ]
.[ 10 111111 ]
.[ 11 000000 ]
.[ 11 111111 ]
subnet 0; broadcast address = 192.168.1.63
subnet 1; broadcast address = 192.168.1.127
subnet 2; broadcast address = 192.168.1.191
subnet 3; broadcast address = 192.168.1.255
11000000.10101000.00000001.00000000
Subnetting (Example): To subnet
a small network

## Slide 86
Subnet 0: 
192.168.1.0/26
192.168.1.[ 00 000000 ]
.[ 00 111111 ]
.[ 01 000000 ]
.[ 01 111111 ]
.[ 10 000000 ]
.[ 10 111111 ]
.[ 11 000000 ]
.[ 11 111111 ]
11000000.10101000.00000001.00000000
00 000001 – first host
00 111110 – last host
10 000001 – first host
10 111110 – last host
Subnetting (Example): To subnet
a small network
01 000001 – first host
01 111110 – last host
11 000001 – first host
11 111110 – last host

## Slide 87
192.168.1.0/24 be divided into 4 subnets we get:
Subnetting (Example): To subnet
a small network

## Slide 88
200.1.0.0/16
161.139.2.0/24
X
Given a network with hosts and interconnecting routers.
What are the subnet mask for the network that consists of host A, B, D and E?
What is the subnet network address of X if the subnet mask is 255.0.0.0?
Get first valid usable IP address for host A, B, D, E and G.
Get last valid usable IP address for each router’s interface at C and F.
Exercise
A
B
D E G
10.90.2.1
C
F
Self study

## Slide 89
200.1.0.0/16
161.139.2.0/24
X
Net. consists of host A, B:
255.255.0.0
Net. consists of host D, E:
255.255.255.0
(b) 10.90.2.1
255. 0.0.0
10. 0.0.0
First valid usable IP address:
A: 200.1.0.1
B: 200.1.0.2
D: 161.139.2.1
E: 161.139.2.2
G: 10.90.2.2
(d) Last valid usable IP address:
C: 200.1.255.254
F: 161.139.2.254
Solution
A
B
D E G
10.90.2.1
C
F
Self study

## Slide 90
Exercise
Given an IP address as 200.23.0.0/20. The network need to be divided into 5 subnets with first subnet label as Subnet 0 and last subnet label as Subnet 4.
What is the original subnet mask for the given IP address network?
How many hosts can be supported in the original IP address network?
List all new subnet address in binary and dotted decimal format.
What is the new subnet mask for each subnet?
How many hosts can be supported for each new subnet?
List the first 5 valid IP addresses for the Subnet 3.
How many subnet remain unused and can be utilized in future?
Self study

## Slide 91
Solution
Solutions:
11111111.11111111.11110000.00000000
255.255.240.0
(b) Total original hosts  212 – 2 = 4096 – 2 = 4094 hosts (12 bit for host portion)
(c) Number of Subnets Needed = 5  nearest 23 = 8 subnets; 3 bits for subnet;
11001000.00010111.00000000.00000000 (200.23.0.0/23)
11001000.00010111.00000010.00000000 (200.23.2.0/23)
11001000.00010111.00000100.00000000 (200.23.4.0/23)
11001000.00010111.00000110.00000000 (200.23.6.0/23)
11001000.00010111.00001000.00000000 (200.23.8.0/23)
11001000.00010111.00001010.00000000 (200.23.10.0/23)
11001000.00010111.00001100.00000000 (200.23.12.0/23)
11001000.00010111.00001110.00000000 (200.23.14.0/23)
Self study

## Slide 92
Solution
Solutions:
(d) 11111111.11111111.11111110.00000000
255.255.254.0
(e) Total hosts in new subnet  29 = 512 – 2 = 510 hosts (9 bits for host portion)
(f) Subnet 3 = 200.23.6.0/23
11001000.00010111.00000110.00000001 (200.23.6.1/23)
11001000.00010111.00000110.00000010 (200.23.6.2/23)
11001000.00010111.00000110.00000011 (200.23.6.3/23)
11001000.00010111.00000110.00000100 (200.23.6.4/23)
11001000.00010111.00000110.00000101 (200.23.6.5/23)
(g) Need 5 subnets, generated subnets = 8, extra = 8 – 5 = 3 subnets for future use
Self study

## Slide 93: Extra Exercise: Subnet small network
Say, Company A (CA) is given the Network address 192.168.1.0/24
CA has 4 departments under it: RND, Sales, Finance, HR
Each department needs the following number of usable host: RND(50), Sales(30), Finance(20), HR(10)
Task:
  Divide equally for all dept. (same/equal size)

## Slide 94
Network address 192.168.1.0/24
to divide into SAME/EQUAL SIZED 4 dept : RND, SALES, FIN, HR
STEP 1 : Divide the Network and host portion (HP)
192 . 168 . 1 . 0
11000000 . 10101000.00000001.00000000
NP = 24 bits
**when subnetting ONLY HOST PORTION
is borrowed from (disturbed)
STEP 2 : Decide how many bits need to BORROW from HP?
4 depts.  4 subnet
So 2x = 4  x = 2 bits
Borrow 2 bits

## Slide 95
Network address 192.168.1.0/24
to divide into SAME/EQUAL SIZED 4 dept : RND, SALES, FIN, HR
STEP 3 : Borrow 2 bits from the host portion
192 . 168 . 1 . 0
11000000 . 10101000.00000001.00000000
Borrow from this end – THE LEFTMOST
STEP 4 : Arrange the new subnets
192 . 168 . 1 . 0
11000000 . 10101000.00000001.00000000 [0]
.00111111 [63]
.01000000 [64]
.01111111 [127]
.10000000 [128]
Within the subnet , the HP gets all 0 and all 1

## Slide 96
Network address 192.168.1.0/24
to divide into SAME/EQUAL SIZED 4 dept : RND, SALES, FIN, HR
STEP 4 : Arrange the new subnets
192 . 168 . 1 . 0
11000000 . 10101000.00000001.00000000
.00111111
.01 000000
.01 111111
.10 000000
.10 111111
.11 000000
.11 111111
S0 Network Add
S0
S1
S2
S3
S0 Broadcast Add
S0 (Subnet 0)
network address:
192.168.1.0
Broadcast address:
192.168.1.63

## Slide 97
Network address 192.168.1.0/24
to divide into SAME/EQUAL SIZED 4 dept : RND, SALES, FIN, HR
STEP 5 : Assign the new subnets
192 . 168 . 1 . 0
11000000 . 10101000.00000001.00000000
.00111111
.01 000000
.01 111111
.10 000000
.10 111111
.11 000000
.11 111111
S0 - RND
S1 - SALES
S2 - FIN
S3 - HR
S0 (Subnet 0)
Usable/valid IP address:
192.168.1.1 to
192.168.1.62
000001
111110
000001
111110
000001
111110
000001
111110

## Slide 98
SUBNET | NETWORK ADDRESS | USABLE/VALID IP ADD. RANGE | BROADCAST ADDRESS | SUBNET MASK
0 | 192.168.1.0 | 192.168.1.1 – 192.168.1.62 | 192.168.1.63 | /26 OR 255.255.255.192
1 | 192.168.1.64 | 192.168.1.65 – 192.168.1.126 | 192.168.1.127 | /26 OR 255.255.255.192
2 | 192.168.1.128 | 192.168.1.126 – 192.168.1.190 | 192.168.1.191 | /26 OR 255.255.255.192
3 | 192.168.1.192 | 192.168.1.190 – 192.168.1.254 | 192.168.1.255 | /26 OR 255.255.255.192
Convert calculation in table to binary format for complete understanding
STEP 6 : Complete the subnetting table

## Slide 99
Obtaining a block of addresses (network address)
Q: How does a network get IP address block for itself (network part of address)
A: ICANN: Internet Corporation for Assigned Names and Numbers (http://www.icann.org/)
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes
ICANN allocates addresses to 5 regional Internet registries (RRs)
  like ARIN, RIPE, APNIC, and LACNIC
  …which handle the allocation/management of addresses within their regions.

## Slide 100
Obtaining a host addresses
Q: How does a host get IP address within its network (host part of address)?
A: local ISP (e.g. Telekom, Celcom, DiGi, Maxis) & local organization like UTM:
DHCP: Dynamic Host Configuration Protocol: dynamically get address from server. “plug-and-play” concept
OR
hard-coded by sysadmin in config file (e.g., /etc/rc.config in UNIX)

## Slide 101
In an organization, IP address can be assigned to host
  Statically – User manually configure IP address at host (normally done by ‘network admin’)
  Dynamically - done using DHCP
DHCP can be configured to assign
  the same IP address to a given host each time it connects to the network
  OR
  different IP address each time the host connects to the network.
Dynamic Host Configuration Protocol (DHCP)

## Slide 102
Goal: allow host to dynamically obtain its IP address from DHCP server when it joins network
  host will lease an IP address, can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who want to join/leave network
DHCP is a plug-and-play protocol
  Makes network admin job easier
  Makes network mobility easier too
Dynamic Host Configuration Protocol (DHCP)

## Slide 103
A newly arriving host, goes through the DHCP protocol four-step process
Dynamic Host Configuration Protocol (DHCP)

## Slide 104: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 105
DHCP 4 steps process
  DHCP server discovery
  DHCP server offer
  DHCP request
  DHCP ACK
DHCP – 4 Steps Process
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg
Notes: DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 106
DHCP server discovery
  newly arriving host needs to find a DHCP server
   done by broadcasting the DHCP discover message
    source: this host 0.0.0.0
    dest: 255.255.255.255 (i.e. broadcast to all)
    UDP: Port 67
DHCP server offer
  DHCP server(s) will respond to the client with a DHCP offer message that is broadcast to all
  A client might receive offers from > 1 DHCP servers
DHCP – 4 Steps Process

## Slide 107
DHCP request
  Client choose from among the offers
  Respond to its selected offer with a DHCP request message.
DHCP ACK
  The server responds to the DHCP request message with a DHCP ACK message, confirming the requested parameters.
DHCP – 4 Steps Process
Notes: In DHCP request message, the client echoes back the configuration parameters.
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 108
DHCP – 4 Steps Process
yiaddr = your IP address

## Slide 109: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 110: DHCP: example
Connecting laptop will use DHCP to get IP address, address of first-hop router, address of DNS server.
router with DHCP
server built into
router
DHCP REQUEST message encapsulated in UDP, encapsulated in IP, encapsulated in Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demux’ed to IP demux’ed, UDP demux’ed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 111: DHCP: example
DCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulated DHCP server reply forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DNS server, IP address of its first-hop router

## Slide 112: DHCP: Example Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
request

## Slide 113: DHCP: Example Assignment (home LAN)
DHCP Server Assignment
TCP/IP Client Setting

## Slide 114: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing information:

## Slide 115: Hierarchical addressing: more specific routes
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Organization 1 moves from Fly-By-Night-ISP to ISPs-R-Us
ISPs-R-Us now advertises a more specific route to Organization 1

## Slide 116: Hierarchical addressing: more specific routes
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
Organization 1 moves from Fly-By-Night-ISP to ISPs-R-Us
ISPs-R-Us now advertises a more specific route to Organization 1
200.23.18.0/23
Organization 1
“or 200.23.18.0/23”

## Slide 117
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
input ports, switching, output ports
buffer management, scheduling
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation (NAT)
  IPv6
4.4 Generalized Forwarding and SDN
  Match+action
  OpenFlow: match+action in action
Chapter 4: data plane

## Slide 118: NAT: network address translation
Q: are there enough 32-bit IP addresses?
ICANN allocated last chunk of IPv4 addresses to RRs in 2011
NAT (next) helps IPv4 address space exhaustion
IPv6 has 128-bit address space
"Who the hell knew how much address space we needed?" Vint Cerf (reflecting on decision to make IPv4 address 32 bits long)

## Slide 119: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network (e.g., home network) 10.0.0/24
138.76.29.7
rest of
Internet
datagrams with source or destination in this network have 10.0.0/24 address for source, destination (as usual)
all datagrams leaving local network have same source NAT IP address: 138.76.29.7, but different source port numbers
NAT: all devices in local network share just one IPv4 address as far as outside world is concerned

## Slide 120: NAT: network address translation
  all devices in local network have 32-bit addresses in a “private” IP address space (10/8, 172.16/12, 192.168/16 prefixes) that can only be used in local network
  advantages:
    just one IP address needed from provider ISP for all devices
    can change addresses of host in local network without notifying outside world
    can change ISP without changing addresses of devices in local network
    security: devices inside local net not directly addressable, visible by outside world

## Slide 121: NAT: network address translation
implementation: NAT router must (transparently):
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
      remote clients/servers will respond using (NAT IP address, new port #) as destination address
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in destination fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 122: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 123: NAT: network address translation
NAT has been controversial:
  routers “should” only process up to layer 3
  address “shortage” should be solved by IPv6
  violates end-to-end argument (port # manipulation by network-layer device)
  NAT traversal: what if client wants to connect to server behind NAT?
but NAT is here to stay:
  extensively used in home and institutional nets, 4G/5G cellular nets

## Slide 124
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
input ports, switching, output ports
buffer management, scheduling
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation (NAT)
  IPv6
4.4 Generalized Forwarding and SDN
  Match+action
  OpenFlow: match+action in action
Chapter 4: data plane

## Slide 125: IPv6: motivation
initial motivation: 32-bit IPv4 address space soon to be completely allocated. IPv6 provided a larger IP address space  more IP address
additional motivation:
  speed processing/forwarding: 40-byte fixed length header
  enable different network-layer treatment of “flows” (QoS)

## Slide 126: IPv6 datagram format
payload (data)
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
priority: identify priority among datagrams in flow
flow label: identify datagrams in same "flow.” (concept of “flow” not well defined).
128-bit
IPv6 addresses

## Slide 127: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label:
labeling of packets belonging to particular flows for which the sender requests special handling
  Example: real-time service, media streaming
  But the real definition of flow is still vague (unclear)
next header: identify upper layer protocol for data
Traffic class:
  used to give priority to datagrams
    certain datagrams within a flow
    datagrams from certain applications (for example, ICMP) over others
Payload length:
  What size of data sent (not including header)
  If payload is 4bytes  total datagram size = 40 + 4 = 44 bytes

## Slide 128: IPv6 datagram format
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
Used to give priority to certain datagrams
increased the size of the IP address from 32 to 128 bits
4-128

## Slide 129: IPv6 datagram format and other changes from IPv4
IPv6 datagram format:
  Header : 40-byte fixed-length header  allows faster processing of the IP datagram
  Fragmentation: NO fragmentation allowed
  options: allowed, but outside of header, indicated by “Next Header” field
  Checksum: NO checksum at Network Layer for faster processing at each hop  use checksum on Transport Layer
  ICMPv6: new version of ICMP
    additional message types, e.g. “Packet Too Big”
    multicast group management functions

## Slide 130: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers (“packet within a packet”)
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 131: Tunneling and encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
IPv4 network
IPv4 network connecting two IPv6 routers

## Slide 132: Tunneling and encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
IPv4 tunnel connecting two IPv6 routers
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
E
F
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
IPv4 datagram
IPv6 datagram
tunneling: IPv6 datagram as payload in a IPv4 datagram
IPv6/v4
IPv6/v4

## Slide 133: Tunneling
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
IPv4
IPv4
E
IPv6/v4
IPv6
F
C
D
A
B
IPv6
IPv6/v4
logical view:
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
Note source and destination addresses!

## Slide 134: IPv6: adoption
Google1: ~ 30% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
1 https://www.google.com/intl/en/ipv6/statistics.html

## Slide 135: IPv6: adoption
Google1: ~ 30% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  25 years and counting!
  think of application-level changes in last 25 years: WWW, social media, streaming media, gaming, telepresence, …
  Why?
1 https://www.google.com/intl/en/ipv6/statistics.html

## Slide 136
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
input ports, switching, output ports
buffer management, scheduling
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation (NAT)
  IPv6
4.4 Generalized Forwarding and SDN
  Match+action
  OpenFlow: match+action in action
Chapter 4: data plane

## Slide 137: Generalized forwarding: match plus action
1
2
0111
3
values in arriving
packet header
Review: each router contains a forwarding table
“match plus action” abstraction: match bits in arriving packet, take action
  generalized forwarding:
    many header fields can determine action
    many action possible: drop/copy/modify/log packet
forwarding table
(aka: flow table)
(aka: flow table)
  destination-based forwarding: forward based on dest. IP address

## Slide 138
Generalized Forwarding and SDN
Kurose, J.F. and Ross, K.W. (2021). Computer Networking: A Top-Down Approach (8th Edition). Pearson Education Limited, England. (pp. 353)
Generalized Forwarding:
Each packet switch contains a match-plus-action flow table that is computed and distributed by a remote controller.
Overview
Notes: Our following discussion of generalized forwarding will be based on Open- Flow [McKeown 2008, ONF 2020, Casado 2014, Tourrilhes 2014]—a highly visible standard that has pioneered the notion of the match-plus-action forwarding abstrac- tion and controllers, as well as the SDN revolution more generally [Feamster 2013]. We’ll primarily consider OpenFlow 1.0, which introduced key SDN abstractions and functionality in a particularly clear and concise manner. Later versions of OpenFlow introduced additional capabilities as a result of experience gained through
implementation and use; current and earlier versions of the OpenFlow standard can be found at [ONF 2020]

## Slide 139
Generalized Forwarding and SDN
Kurose, J.F. and Ross, K.W. (2021). Computer Networking: A Top-Down Approach (8th Edition). Pearson Education Limited, England. (pp. 353)
Generalized forwarding will be based on a standard rule  Open-Flow.
It is a highly visible standard that has pioneered the notion of the match-plus-action forwarding abstraction and controllers.
OpenFlow1.0 is used, which introduced key SDN abstractions and functionality
Overview

## Slide 140: Flow table abstraction
flow: defined by header field values (in link-, network-, transport-layer fields)
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Router’s flow table define router’s match+action rules
Flow table
match
action

## Slide 141: Flow table abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Flow table
match
action
1
2
3
4
* : wildcard
src=10.1.2.3, dest=*.*.*.* send to controller
src=1.2.*.*, dest=*.*.*.* drop
src = *.*.*.*, dest=3.4.*.* forward(2)

## Slide 142: OpenFlow: flow table entries
Match
Action
Stats
Forward packet to port(s)
Drop packet
Modify fields in header(s)
Encapsulate and forward to controller
Packet + byte counters
Header fields to match:
Ingress Port
Src MAC
Dst MAC
Eth Type
VLAN
ID
IP
ToS
IP Proto
IP Src
IP Dst
TCP/UDP Src Port
VLAN
Pri
TCP/UDP Dst Port
Link layer
Network layer
Transport layer

## Slide 143
Layer 2 frames from MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
Destination-based forwarding:
* * * * * * * * * * *
51.6.0.8
port6
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
OpenFlow: Example
Examples 1
Action
Destination-based layer 2 (switch) forwarding:
22:A7:23:
11:E1:02
* * * * * * * * * * *
port3
Action

## Slide 144
Firewall:
* * * * * * * * * * *
22
Drop
OpenFlow: Example
Examples 2
Action
Block (do not forward) all datagrams destined to TCP port 22
* * * * * * * * * * *
Drop
Action
128.119.1.1
Block (do not forward) all datagrams sent by host 128.119.1.1

## Slide 145
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
match+action: abstraction unifies different kinds of devices
OpenFlow: Abstraction

## Slide 146: OpenFlow example
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2
Examples 3

## Slide 147
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2
OpenFlow: Example
Examples 3